## Slide 1: Protecting Sewer Capacity While Supporting Community Growth
Panel Discussion –CT COST 2025 Fall Conference
Moderated by: Kat Young, H2M

## Slide 2: Panelists for Today’s Panel
Ted Donoghue, Superintendent, Litchfield WPCA
Alex Czerwinski, Technical Sales Engineer, Savy & Sons
Ben Rukavina, Key Account Manager, ADS Environmental Services
Norb Church, Esquire and Founder, Church and Church
Martin Heft, Undersecretary, Office of Policy and Management, State of CT
Greg Levasseur, PE, CT Office Director, Vice President, H2M Architects + Engineers
Eric Hess, Sales Manager, F.R. Mahony & Associates
Protecting Sewer Capacity While Supporting Community Growth

## Slide 3: Panel Discussion Format
Key Definitions and Concepts
Preliminary Topics Discussion
Questions from Attendees

## Slide 4: Inflow & Infiltration
Combined - they place a burden on collection systems and wastewater treatment facilities.
And, limit available capacity for new development
Definition
Infiltration occurs when groundwater seeps into sewer pipes through cracks, leaky pipe joints and/or deteriorated manholes.
Inflow is stormwater that enters the sewer system through rain leaders, basement sump pumps or foundation drains illegally connected to the sewer

## Slide 5
I & I Reduction Strategies
Case Study

## Slide 6: I & I Reduction Strategies
Proactive inspection and data collection
Targeted rehabilitation using trenchless technologies
Sealing manholes and service laterals
Ongoing maintenance to prevent reoccurrence
By investing in these practices, municipalities can extend system life, reduce treatment costs, and plan confidently for future growth.

## Slide 7: Flow Monitoring
$1
Billion
Flow Meters
Battery Powered
Wireless Telemetry
Intrinsically Safe:
Objectives
Inflow & Infiltration Assessment
Capacity Analysis
Model Calibration
Billing Networks

## Slide 9: Hydraulic Modeling – Key Steps

## Slide 10: Determining Sewer Capacity with Hydraulic Modeling
Physical Pipe Network Info
Current & Projected Flows
Pipe locations
Pipe sizes
Slope
Pipe material
GIS/AM system
Inverts
Lengths
Metering data
Pump station data
Plant data
Estimations using lot count and use types
Wet weather flows
Projecting for growth

## Slide 11: Sanitary Sewer Models
Contoso
Our product is priced below that of other companies on the market
Design is simple and easy to use, compared to the complex designs of the competitors
Affordability is the main draw for our consumers to our product
Hydrodyamic Model Realworld conditions including backwater, flow reversal, surcharges utilizing St. Venant equations.
Requires dedicated software.
Manning’s Equation Model Accounts for pipe slope and diameter only. No upstream or downstream effects are considered.
Can be performed directly in GIS, excel, or on paper.

## Slide 12: Sewer Availability What Information is Needed?
Considerations for Reviewers
Is connection in-district or out-of-district
Known O&M issues downstream of connection point
Capacity limitations of downstream sewers, pump stations or treatment facilities
Non-standard flows or waste strengths
Pretreatment or equalization requirements
What to do when sewer service is not available?
Upgrade or extend sewer system and/or treatment capacity
Alternative on-site treatment systems
Flow studies

## Slide 13: Types of Models
Steady State Workbook
Limited scope or complexity Useful for locations with minimal data
Steady State Software
Accomodates larger networks, scenarios Good outputs for public communication
Dynamic Model
Complex situations, projections Demands more intensive data input

## Slide 14: Sewer Availability Process
Tracking and Mapping is Essential

## Slide 15
Connecticut offers various funding opportunities for sewer projects through the Clean Water Fund and other state initiatives.
These funding opportunities are designed to help Connecticut communities improve their sewer infrastructure and address water quality needs.
It is essential to check the eligibility criteria and application processes for each funding opportunity.

## Slide 16: SMALL TOWN ECONOMIC ASSISTANCE PROGRAM
Preserving the historical integrity and beauty of our small towns is vital to our economy and quality of life. The Small Town Economic Assistance Program (CGS Section 4-66g) funds economic development, community conservation and quality-of-life capital projects for localities that are ineligible to receive Urban Action (CGS Section 4-66c) bonds.
This program is managed by the Office of Policy and Management and grants are administered by various state agencies.

## Slide 17: SMALL TOWN ECONOMIC ASSISTANCE PROGRAM

## Slide 18: SMALL TOWN ECONOMIC ASSISTANCE PROGRAM
Priority project areas include shovel-ready projects and pollution control (water, waste, energy)in order to reduce costs and environmental impacts.

## Slide 19: SMALL TOWN ECONOMIC ASSISTANCE PROGRAM
Year | Town Name | Project Description | Grant Amount | Agency
2005 | Cromwell | Sanitary sewer and utility improvements for commercial | $ 500,000 | DECD
2005 | North Haven | Upgrade of sewer lines and road to industrial park | $ 386,000 | DECD
2006 | Bolton | The Bolton Lakes sewer capital project | $ 150,000 | OPM
2007 | Bolton | Bolton Lakes sewer capital project | $ 200,000 | DEEP
2007 | North Branford | The installation of sanitary sewers along Route 80 | $ 250,000 | DEEP
2008 | Bolton | Bolton Lakes sewer capital project | $ 100,000 | DEEP
2010 | Bolton | Bolton Lakes sewer capital project | $ 200,000 | DEEP
2010 | Colchester | Development of engineering and cost information for municipal sewer and water improvements | $ 130,000 | DEEP
2010 | New Hartford | Repair of two sewer lines located in the downtown vicinity | $ 250,000 | DEEP
2010 | Norfolk | Extension of water and sewer lines to service the Town Garage and a planned affordable housing project | $ 250,000 | DEEP
2010 | Tolland | Extension of 5,000 feet of sanitary sewers in the Neighborhood Commercial Zone | $ 200,000 | DEEP
2010 | Windsor Locks | Chestnut Street partial road, drainage, sewer and sidewalk project | $ 65,838 | DOT
2010 | Windsor Locks | Church Street road, drainage, sewer and sidewalk project | $ 150,000 | DOT
2011 | Bolton | Construction and installation of off-site wastewater disposal and sewer service in Bolton Lakes area | $ 200,000 | DEEP
2011 | New Hartford | Repair and reconstruction of existing sewer line along Main Street | $ 150,000 | DEEP
2011 | Sharon | Construction of a new septic line from the town highway garage to the municipal sewer | $ 50,000 | DEEP
2011 | Sharon | Connection of the dog pound to the municipal sewer | $ 5,000 | DEEP
2011 | Stafford | High Street Road and sidewalk reconstruction, drainage improvements and sewer line replacement | $ 200,000 | DOT
2012 | Bethel | Reconstruct and repave roads impacted by the Stony Hill sewer extension | $ 500,000 | OPM
2012 | East Haddam | Rehabilitate, repair East Haddam Water Pollution Control Authority | $ 100,000 | DEEP
2012 | Ellington | Sewer extension along Route 30 | $ 75,000 | DEEP
2014 | Newtown | Hawleyville sewer extension project | $ 500,000 | DEEP
2015 | Stafford | Extend Public Water Line and Sewer to accommodate Avery Park Housing Project | $ 500,000 | DOH
2016 | Bozrah | Sanitary Sewer Wastewater | $ 500,000 | DEEP
2020 | Haddam | Higganum Community Sewer Project | $ 128,205 | DPH
2022 | Avon | Route 44 Sanitary Sewer Pump Station Rehabilitation | $ 500,000 | DEEP
2022 | Bolton | Construction of Sanitary Sewer Main | $ 500,000 | DPH
2022 | Brookfield | Brookfield Market Area Sewer System | $ 500,000 | DEEP
2023 | Harwinton | WPCA Sewer Collection System Rehabilitation | $ 464,000 | DEEP

## Slide 20: Intermunicipal Sewer Agreements
Legal contract between two or more municipalities that establishes a framework for them to cooperatively manage their sewer systems, including financing, building, and operating treatment work

## Slide 21: Sewer Connection Moratorium
A temporary suspension of new sewer hookups, often imposed when a municipal sewer system reaches its capacity due to growth or system failures

## Slide 22: Biologically Active Filter (BAF) Technology
Attached growth/fixed film biological treatment
Also known as Submerged Attached-Growth Bioreactors (SAGBs)
Combines biological treatment and filtration mechanisms to remove contaminants
Basic contaminant & nutrient removal inside filters include:
  BOD5
  TSS
  TN
  Total Phosphorus (TP) with coagulant addition

## Slide 23: Biologically Active Filter (BAF) Process
Typical BAF Process
Anoxic/Equalization Tank
BAF Reactor Tank
Clearwell Tank
•Exterior tankage
•Typically, below grade
Site constraints
Minimal visual impact

## Slide 24: Where Pressure Sewers are Used
Septic to sewer backlog projects
New home development
Challenging land
Expand the service area of an existing collection systems
Failed gravity, eliminate I/I
90% Residential | 10% Commercial

## Slide 25: Advantages – Pressure Sewer Systems
Pressure Sewer does not have central critical infrastructure. A fault at one site will not affect the operation at other sites
Pressure Sewer sites can identify system abusers - debris or infiltration more effectively than vacuum or gravity systems
Pressure sewer systems have zero storm water infiltration which significantly reduces the burden on downstream infrastructure
Reduce Capitol Expense and O&M

## Slide 26: Keys to Design
Layout of lots to be served (plat or topo map)
Potential flows per connection/lot
Pipe type (typically SCH40 PVC, SDR26 PVS, SDR11 HDPE, SDR21 PVC – min. 160 psi rated)
Topographical information
Discharge location or end of the pressure sewer system
Climate (frost depth, etc.)
Code requirements
Any other relevant information regarding geography, flows, site conditions, requirements, etc.

## Slide 27: THANK YOU FOR YOUR ATTENTION AND THOUGHTFUL QUESTIONS